Eddy covariance data - post processing (after flux calculation by Eddypro)
Olivier Marloie, July 2014 - Adaptation to the Font-Blanche Site

R3 sonic anemometer and LI-7500 open path analyser

Quality check realised by Eddypro (Mauder and Foken 2004 , 0-1-2 system)
SSITC_TEST

HARD FILTER

1 - Failures on LI7500
DIAG_IRGA = CHOPPER_LI7500 + DETECTOR_LI7500 + PLL_LI7500;
DIAG_IRGA > 0

2- Range Filter

Variable	min	max
CO2	320	550
FC	-40	20
H2O_CONC	0.4	2830*
LE	-100	600
T_SONIC	248	323
H	-200	800
TAU	-5	0
WS	0	30
USTAR	00000001	2.5
ZL	-50	50
SH_EC	-30	30
SLE_EC	-80	80
SC_EC	-1	1

* Max for TA = 40°C and RH = 100%

3- Variance of CO2
CO2_hf (CO2_VAR > 0.16) = NaN;

4 - LI7500 - Rain filter
FC_hf, CO2_hf
LE_hf, H2O_hf

SOFT FILTER
1 - Range Filter
Variable	min	max
CO2	320	450*
H2O	0.5	30*

* Max established from the annual evolution observed on the site
2 – Variance of Sonic Temperature
H_sf (T_SONIC_VAR > 4) = NaN; % T_SONIC_VAR :

3- Spikes detection and filter
Low frequency spikes detection and filtering based on median diurnal variations
CO2_sf = mdv_filter(CO2_sf,2,1,30,0);

4- Spikes detection on half hour data during night
Shape filter on H, LE, FC : if spike flag = 1

5- High values of w
Quality flag for high values of w according to CarboEurope methodology
flagw = 2 if w unrotated > 0.35 m.s-1

6- Integral Turbulence Characteristic
Quality flag according to integral turbulence characteristic test (Foken et al. 1996)
ITC_FLAG
0 : good
1: exceeding 30% is deemed as the absence of well-developed turbulence conditions
2 : exceeding 100%, very bad

7- Footprint filter
Footprint model : Kljun et al. (2004)
FOOTPRINT_FILTER = 1; % OK
SI (FETCH_90 > FOOTPRINT_THRESHOLD) then FOOTPRINT_FILTER = 0;

8- USTAR Threshold
 U* threshold detection according to Reichtein et al. 2005
USTAR_TEST = 2 when USTAR < Threshold